SIMULATION OF POWER DISTRIBUTION MANAGEMENT

System Description:

Power Distribution Management (PDM) is a system responsible for ensuring that the consumers have undisrupted power supply. They are also known as Electricity Distribution systems and the main purpose of the system is to supply electrical energy from the substation to the consumer locations. To improve transmission efficiency and to comply with consumer needs, the transmission voltage may be stepped-up or stepped-down. A whole network of routers, circuit breakers, switches, alarms, load-reading meters, telemetry etc. [3] are used for electricity distribution and supply. Also companies share National grids for power distribution and supply.

The Control Engineers (CE) with the assistance of Field Engineers (FE) does the management of these power distribution networks. The Control Engineers has to ensure that losses in the electricity transmission is kept minimal and all consumers are supplied an undisrupted power supply by maintaining an optimal power grid configuration [6]. This optimal configuration can be maintained by reducing the transmission losses, preventing overloads and by proper switching of networks. The whole PDM system and the simulation act as an aid to the CE in order to maintain and carry out the electricity distribution system requirements.

One of the important requirements in order to achieve the above goal is to promptly respond to the emergencies that may arise due to system faults and also to carry out the maintenance work in a planned fashion. CE must be able to monitor the whole system and information must be available from all the events and external systems associated with the network [1]. The customers may be high voltage consumers like factories or low voltage consumers like independent households. Irrespective of the consumer types, PDM must be able to satisfy their needs and should be able to deliver an uninterrupted power supply. The simulation should help CE achieve this goal by monitoring the network, simulating the electricity transmission and showing the fault locations and blackout areas in the network, [5] by activating alarms and sharing information between various agents in the PDM.

Requirements:

A simulator for electricity distribution management must consider all the factors in the transmission network that can make the work of CE easier. This will integrate the existing systems as well as the new systems that may improve the overall system management and information sharing. The important requirements [2], [4] that has to be considered while designing a simulator for PDM are given below:

- Identifying faults on network: Faults may be due to overloading, switching failure, third party damage, equipment failure, industrial actions, disasters or lightening. (G0)

- Analyze faulty network (G1)

  - Log load readings and database: It will help to analyze if there was any switching failure or overload in faulty network. (G1.1)

  - Collect information about lightning strikes and weather conditions by implementing a Weather Watch Agent (WWA) (G1.3)

  - Implement an Information Agent (IA) that has static information about connectivity of pieces of plant, and dynamic information like state of circuit breakers and switches. (G1.2)

  - Implementing a Telemetry Agent (TA) to receive telemetry, convert it to standard format and to send data to different agents on request. Telemetry data is only present at the point where there is a join between low voltage and high voltage network. (G2.1.1)

- Determine the type of fault (G2)

  - A High Voltage Expert System (HVES) and a High Voltage Diagnosis Agent (HVDA) to diagnose the location, time and type of high voltage fault on the electricity network. (G2.1) (G2.1.2)

  - A Low Voltage Expert System (LVES) and a Low Voltage Diagnosis Agent (LVDA) to get information from customer telephone calls, to load LV network data and network state. (G2.2) (G2.2.1) (G2.2.2)

- Isolate and fix the faulty section (G3)

  - Automatic operation of circuit breakers (G3.1)

  - Remote switching operation in response to faults (G3.2)

  - Coordinate with FE in locations where remote operation is not available (G3.3)

- Simulate breakers and relays to analyze faults and alarm messages

- A control System interface to act as a front end between the main computer and the other sub systems and agents.

References:

- L.Z. Varga, N.R. Jennings, D. Cockburn, “Integrating Intelligent Systems into a    Cooperating Community for Electricity Distribution Management”, International Journal of Expert Systems with Applications, 1994.

- N.R. Jennings, “The ARCHON System and Its Applications”, Second International Working Conference on Cooperating Knowledge Based Systems, 1994.

- D. Cockburn, N.R. Jennings, “ARCHON: A Distributed Artificial Intelligence System for Industrial Applications”, John Wiley Sixth-Generation Computer Technology Series, 1996

- D. Cockburn, L.Z. Varga, N.R. Jennings, “Cooperating Intelligent Systems for Electricity Distribution”, International Journal of Expert Systems with Applications, 1994

- T. Wittig, N. R. Jennings and E. H. Mamdani, “ARCHON: framework for intelligent co-operation”, Intelligent Systems Engineering, 1994

- L. Panait and S. Luke, “Cooperative Multi-Agent Learning: The State of Art”, Autonomous Agents and Multi-Agent Systems, 2005

- Y. Yamaguchi, Y. Shimoda and M.Mizuno, “Development of District Energy System Simulation Model Based on Detailed Energy Demand Model”, Proceeding of Eighth International IBPSA Conference, 2003

# Footnotes

National Grid is the high voltage electricity transmission network in Great Britain. It connects the major power stations and substations to distribute the electricity generated elsewhere.